## Slide 1: HPLC MS analysis of polymerization
Outline:
  Overview of RNA polymerization form 2’,3’, cyclic nucleotides
  An overview of chromatographic techniques, with a focus on HPLC
  Why we need MS analysis for the polymerization?
  An overview of MS techniques, with a focus on ESI-ToF
  Walk through the Data analysis pipeline

## Slide 2: HPLC MS analysis of polymerization
RNA oligomerization from
2′,3′-cyclic nucleotides in a dry state
Dass et al., ChemSystemsChem, 2022,e202200026
cNMP: C < A < U < G
cNMP + Val: C > A > U > G

## Slide 3: HPLC MS analysis of polymerization
Nucleotide - 10 mM
Amino acid - 50 mM
pH 10 (with KOH)
Dry 20 h

## Slide 4: HPLC MS analysis of polymerization
Nucleotide - 10 mM
Amino acid - 50 mM
pH 10 (with KOH)
Dry 20 h

## Slide 5: HPLC MS analysis of polymerization
HPLC: High Performance liq. chromatography

## Slide 6: HPLC MS analysis of polymerization
HPLC: High Performance liq. chromatography

## Slide 7: HPLC MS analysis of polymerization
HPLC: High Performance liq. chromatography

## Slide 8: HPLC MS analysis of polymerization
HPLC: High Performance liq. chromatography
Lets do chromatography!

## Slide 9
HPLC: High Performance liq. chromatography
Stationary Phase
Mobile Phase
Aqueous buffers
Salt Solutions
Acid/Base Solutions
Organic Solvents
Competing molecule
…

## Slide 10
HPLC: High Performance liq. chromatography
Based on the bed
Column
Planar
TLC
Paper
Based on the phase
Gas
Liquid
HPLC
SFC (Supercrit. Fluid)
Mechanism of Separation
Affinity
Ion Exchange
Size Exclusion
Hydrophobicity
Chromatography

## Slide 11: HPLC MS analysis of polymerization
HPLC: High Performance liq. chromatography
Reverse Phase Ion-Pairing Chromatography
Not the NORMAL phase
Stationary Phase: Hydrophobic
Mobile phase: Hydrophilic
Added to the Mobile phase
Creates a bridge between the Stationary Phase and the Sample
Stationary Phase: C18 Column
Mobile Phase: Water and Methanol system with
Ion Pairing agent: Tri ethyl ammine (TEA)

## Slide 12: HPLC MS analysis of polymerization
Mobile Phase composition:
200mM HFIP (Acid) and 8mM TEA(Base)
Gradient of Methanol concentration.

## Slide 13: HPLC MS analysis of polymerization
Mobile Phase composition:
200mM HFIP (Acid) and 8mM TEA(Base)
Gradient of Methanol concentration.

## Slide 14: HPLC MS analysis of polymerization: Why?
HPLC Chromatogram of
Polymerization reaction G+C+A+U + 2.5X Valine pH 10, 20h @ room temp
4
5
6
7 …

## Slide 15
GCAU 4mers

## Slide 16
GCAU 4mers

## Slide 17
HPLC MS: Mass Spectrometry

## Slide 18
HPLC MS: Mass Spectrometry
Ionization:
Matrix Assisted Laser Desorption ionization (MALDI)
Atmospheric Pressure Chemical Ionization (APCI)
Electrospray Ionization (ESI)
…

## Slide 19
HPLC MS: Mass Spectrometry
Ionization:
Matrix Assisted Laser Desorption ionization (MALDI)
Atmospheric Pressure Chemical Ionization (APCI)
Electrospray Ionization (ESI)
…
Mass selection:
Triple Quadrupole mass filter
Orbitrap/ cyclotron resonance
Time-of-Flight
…

## Slide 20
HPLC MS: Mass Spectrometry
Ionization:
Matrix Assisted Laser Desorption ionization (MALDI)
Atmospheric Pressure Chemical Ionization (APCI)
Electrospray Ionization (ESI)
…
Mass selection:
Triple Quadrupole mass filter
Orbitrap/ cyclotron resonance
Time-of-Flight
…
Detection

## Slide 21
HPLC MS: Mass Spectrometry
Ionization:
Matrix Assisted Laser Desorption ionization (MALDI)
Atmospheric Pressure Chemical Ionization (APCI)
Electrospray Ionization (ESI)
…
Mass selection:
Triple Quadrupole mass filter
Orbitrap/ cyclotron resonance
Time-of-Flight
…

## Slide 22
HPLC MS: Mass Spectrometry
Ionization:
Matrix Assisted Laser Desorption ionization (MALDI)
Atmospheric Pressure Chemical Ionization (APCI)
Electrospray Ionization (ESI)
…

## Slide 23
HPLC MS: Mass Spectrometry

## Slide 24
HPLC MS: Mass Spectrometry
Mass selection:
Triple Quadrupole mass filter
Orbitrap/ cyclotron resonance
Time-of-Flight
…

## Slide 25: HPLC MS analysis of polymerization: How?
HPLC Chromatogram of
Polymerization reaction G+C+A+U + 2.5X Valine pH 10, 20h @ room temp
4
5
6
7 …

## Slide 26: HPLC MS analysis of polymerization: How?
HPLC Chromatogram of
Polymerization reaction G+C+A+U + 2.5X Valine pH 10, 20h @ room temp
4
5
6
7 …

## Slide 27: HPLC MS analysis of polymerization: How?
C38H45N15O29P4 4-

## Slide 28: HPLC MS analysis of polymerization: How?
C38H47N15O29P4 2-
-2 Charge
H+
H+

## Slide 29: HPLC MS analysis of polymerization: How?
HPLC Chromatogram of
Polymerization reaction G+C+A+U + 2.5X Valine pH 10, 20h @ room temp
4
5
6
7 …

## Slide 30: HPLC MS analysis of polymerization: How?
All the 4 mers in the -2 charge states

## Slide 31: HPLC MS analysis of polymerization: How?
C38H47N15O29P4 2-

## Slide 32: HPLC MS analysis of polymerization: How?
C38H47N15O29P4 2-

## Slide 33: HPLC MS analysis of polymerization: How?
C38H47N15O29P4 2-
-2 Charge
H+
H+